## Slide 1: COVID-19 Accessible Testing - Best Practices
Rapid Acceleration of Diagnostics Tech (RADx)
February 28, 2023

## Slide 2: Presenters
  Brian Walsh, RADx Accessibility Program Manager, Deployment Core Team Lead
  Clair O'Donovan, RADx Team Lead
  Emily Kennedy, RADx Project Facilitator
John Blackwood, RADx Team Lead

## Slide 3: RADx Accessibility Team
Clair O'Donovan, RADx Team Lead
Mia Cirrincione, RADx Project Facilitator
Sam Dolphin, RADx Project Facilitator
Maren Downing, RADx Project Facilitator
Emily Kennedy, RADx Project Facilitator
Kevin Leite, RADx Director Commercialization Support
Shaun Moshasha, RADx Project Facilitator
Kim Noble, RADx Communication Lead
Adam Samuta, RADx Project Facilitator
Sal Strods, RADx Team Lead

## Slide 4: Overview
RADx Program Overview
Testing Workflow
Best Practices
Instructions & Digital Design
Company Perspective
Slide 4

## Slide 5: RADx Program Overview
Slide 5

## Slide 6: NIH's Rapid Acceleration of Diagnostics (RADx)
  Goal: Speed innovation in the development, commercialization, and implementation of technologies for COVID-19 testing
    Over 4 Billion tests/products
    45 FDA authorized tests
    1st Over-the-Counter test for use at home
    >100 organizations supported
Reference: https://www.nibib.nih.gov/covid-19/radx-tech-program
Slide 6

## Slide 7: Listening Session....The Beginning
March 2022
  Goals:
  Understand challenges to the accessibility of at-home tests
  Discuss potential improvements, including their potential timescale
  Open lines of communication for ongoing discussion
  Key User Populations:
  No-vision and low-vision
  Fine motor skill difficulties
  Aging population
Advocacy Attendees:
Alliance on Aging and Vision Loss (AAVL)
American Council of the Blind (ACB)
American Foundation for the Blind (AFB)
American Geriatrics Society (AGS)
Independence Through Enhancement of Medicare Coalition (ITEM)
National Disability Rights Network (NDRN)
National Federation of the Blind (NFB)
World Institute on Disability (WID)
Slide 7

## Slide 8: Accessibility Best Practices
Extremely limited standards or guidance
Rich information & learnings emerged from RADx Tech Accessibility Program
Learnings would perish when the program expires
Best Practices Initiative
    Objective: Capture and leverage learnings and experience from the RADx Tech Accessibility Program for current and future tests
    Provide a roadmap for industry to build more accessible products
        Document learnings & process
        Validation of design concepts
        Execute process and resources to ensure effectiveness
    Target Audience: Commercial manufacturers and designers
Slide 8

## Slide 9: Best Practice Content and Testing Workflow
Slide 9

## Slide 10: Testing Workflow
  Strive for complete solutions from product acquisition through disposal
PURCHASE | UN-BOX | SAMPLE COLLECTION | SAMPLE HANDLING | RUN TEST | READ RESULTS | DISPOSAL
Labeling Packaging | Labeling Packaging | Swabs and sample collection Liquid containers Packaging Instructions | Liquid transfer Cassette/ Test Reader Packaging Instructions | Cassette/ Test Reader Instructions Connecting components digitally Test analysis | Test analysis Communicating results Cassette/ Test Reader Connecting com-ponents digitally | Disposal of components Instructions
  General topics across all categories: Holistic Design, Regulatory, Design Control, Braille, and Engaging End Users
Slide 10

## Slide 11: Packaging: Identification
Outer box device packaging is the initial introduction to the User.
Issues
  Much of standard packaging is filled with random information
  QR codes are often missing or insufficiently sized
  No tactile features
Recommendations
  Key information includes brand name, device type, expiration date, links to instructions, and customer service phone number
  QR codes should be easily identifiable
  Provide a means to tactilely find encoded information (e.g., a raised sticker, or raised outline)
Slide 11

## Slide 12: Packaging: Accessing Contents
Contents must be accessible to Users
Issues
  Too much force is required to open
  Hard to access contents
  Tamper-proof labels
    Many users resort to external tools such as scissors, knives, etc.
Recommendations
  Do not require user to apply in excess of five pounds force
  Top of box should open wide for easy access to contents
  Provide familiar tactile cues on the packaging
Note: Make packages resealable if >1 test is included​
Slide 12

## Slide 13: Sample Collection
Swabs for sample collection are a universal opportunity for improvement
Cost sensitive: Off-the-shelf standard parts from large-scale manufacturers
Must balance short-term and long-term solutions
Issues
  Is it obvious which end to open?
  Packaging may inadvertently open the sterile end of the swab
  Swabs with no clear indications for handling may be misused
Recommendations
  Swabs should have identifiable features (e.g., colors, shapes, textures) so that the user knows where to grasp, preventing sample contamination
Slide 13

## Slide 14: Liquid Containers
Vials are multi-purpose - hold liquid as well as receive the swab and sample
Facilitates docking and provides means for gross or precision liquid handling
Issues
  Caps are small and can be easily misplaced
  Caps can be difficult to remove
  Liquid vials can be easily tipped over
Recommendations
  Attach the cap to the liquid vial
  Incorporate a stand for stability or a freestanding tube with wide base
  Vial opening should be large enough to receive sample
Slide 14

## Slide 15: Liquid Transfer
Accurate liquid transfer is critical to successful assay function
Issues
  Liquid transfer from one location to another creates a spill risk
  Error-free counting of drops for sample preparation is challenging
Recommendations
  Eliminate precision liquid transfer when possible
  Design the test to use the entire contents of the fluid vial
  Consider docking of parts where possible
  Focus on instructions
Slide 15

## Slide 16: Cassette and Test Reader
Some tests are self-contained
Some tests use reader technologies – stand-alone readers, smartphones, or readers paired to smartphones
Words matter – terms used interchangeably cause confusion (Analyzer vs. Reader)
Slide 16

## Slide 17: Cassette and Test Reader
Readers may use nonvisual indicators to help guide test taking & results reporting
  Examples: audible beeps, audible voice, haptic feedback
  Generally audible voice and haptic feedback is optimum solution
Using smartphones as the only reader
  Not everyone has a smartphone (e.g. aging population, economically disadvantaged)
  Orientation for taking photos is important
  Use technology that already exists (i.e., "familiar")
  Provide auditory/haptic device positioning and camera visibility feedback (e.g., "test identified"; "failed - move closer"; "failed - increase brightness")
  Standalone readers with optional smart technology preferred
Slide 17

## Slide 18: Instructions & Digital Design
Slide 18

## Slide 19: GEORGIA TECH HOMELAB USABILITY analysis
All products had issues related to instructions
Instructions was the greatest area of deficiency (48% of recommendations)
HomeLab Task Analysis
Product | ​​Total Tasks​​ | Essential Tasks​​ | Inaccessible Essential Tasks​​
A | 36 | 30 | 17 (56.7%)
B | 38 | 29 | 12 (41.4%)
C | 64 | 51 | 18 (35.3%)
D | 41 | 31 | 20 (64.5%)
E | 45 | 37 | 20 (54.1%)
F | 42 | 33 | 16 (48.5%)
G | 74 | 66 | 22 (33.3%)
H | 36 | 32 | 16 (50.0%)
I | 43 | 32 | 19 (59.4%)
J | 44 | 39 | 13 (33.3%)
K | 44 | 34 | 16 (47.1%)
L | 42 | 35 | 16 (45.7%)
M | 76 | 61 | 20 (32.8%)
N | 42 | 34 | 16 (47.1%)
O | 43 | 32 | 16 (50.0%)
HomeLab Recommendations
Product | Total Recommen-dations | Instructions Related Recommendations
A | 18 | 14 (77.8%)
B | 16 | 12 (75.0%)
C | 25 | 15 (60.0%)
D | 23 | 13 (56.5%)
E | 16 | 8 (50.0%)
F | 26 | 13 (50.0%)
G | 20 | 10 (50.0%)
H | 22 | 10 (45.5%)
I | 14 | 6 (42.9%)
J | 21 | 9 (42.9%)
K | 17 | 7 (41.2%)
L | 28 | 11 (39.3%)
M | 20 | 7 (35.0%)
N | 23 | 7 (30.4%)
O | 10 | 3 (30.0%)
Slide 19

## Slide 20: Instructions - Printed
Issues
  Text features (size, font type, italics, and color contrast) are critical
  Steps requiring multiple actions are challenging to follow.
  Blocks of text are sometimes shown in different layouts.
Recommendations
  Use sans serif font, minimize italics, minimum size 14 font, use appropriate contrast ratio and line thickness
  Provide a single, actionable task for each step
  Use a consistent layout. A column style layout works best
Slide 20

## Slide 21: Instructions – Digital
Digital instructions screen reader compatibility
  Screen Reader – software program or application enabling no-vision or low-vision users to convert text displayed on a computer screen, tablet or phone into synthesized speech or refreshable braille display.
    Windows – JAWS & NVDA
    MacOS, iOS, tvOS – VoiceOver
    Android phones, tablets, and kiosks – TalkBack
All images must have meaningful, descriptive alternative ('alt') text
  E.g., describing test components such that they can be discerned from one another non-visually
Web Content Accessibility Guidelines (WCAG) 2.1 AA and PDF/UA standards
  Section 508 and WCAG 2.1 AA compliance is the legal requirement
Slide 21

## Slide 22: Digital Design
Smart Technology
User interfaces (UI) significantly impact usability - small improvements have major impacts
  Provide options to review content in both landscape and portrait orientations.
  Errors, warnings, and success messages do not automatically disappear until user acknowledges message
Operating system (OS) compatibility
  Content must be recognized & understood by computer, smartphone, and tablet OS & accessibility tools.
  Ensure application recognizes and supports built-in device OS accessibility settings
Other Modalities
Audio instructions - human voiceover is preferred or clear text-to-speech (TTS) engines
Audible phone instructions - IVR systems connect users to instructions through a phone call
Video instructions with multilingual closed captions
Slide 22

## Slide 23: Company Perspective
Slide 23

## Slide 24: Different Reactions from Different Types of Organizations
Company willingness to engage with the RADx Accessibility Program – Responses differ depending on type of organization
  Multinational Publicly Traded Diagnostics Company
  Privately Held Small Company with Limited Portfolio
  Start Up Entity with Technology that Could A True Advance in Accessible Testing
Slide 24

## Slide 25: Multinational Publicly Traded Diagnostics Company
Meeting #1 - “We are interested to learn more”
Meeting #2 - “We want to be responsive but give us some time to review with management”
Meeting #3 – “This is interesting. We already build into our products a lot of Accessibility features”
Meeting #4 – “You know. We unfortunately have other things we need to spend our time and money on right now and while this is interesting and important; we must decline”
Slide 25

## Slide 26: Privately Held Small Company with Limited Portfolio
Meeting #1 – “ This is excellent – tell us more”
Meeting #2 – “When can we send you documents and materials to review”
Meeting #3 – “We are ready, willing and able to adapt our product so that it is as highly accessible as we can make it.
Meeting #4 – “Let’s proceed with recommended changes. The only caveat is that if a change would lead to a ‘form, fit or function’ design change we want to be careful not to trigger the need for a new clinical trial. That is the line we have to be careful not to not cross by accident. But we are open to it if it make sense. Everything else is good to go”
Slide 26

## Slide 27: Start Up Entity with Technology that Could Make A True Advance in Accessible Testing
Meeting #1 – “We could have applied for Advanced Testing, but our intuition was that this is uniquely suited for Accessibility”
Meeting #2 – “Thanks for taking us through the program and guiding us. We really want to make this a product that can serve those with challenges using other types of products
Meeting #3 – “We want to succeed and are willing to adjust our project. We are not experts in everything that goes into Accessibility Design - will need help.
Slide 27

## Slide 28: Key Takeaways
Slide 28

## Slide 29: Key Takeaways
Accessible design extends through the entire product experience from acquisition to disposal
Requirements for an accessible design are best developed in cooperation with those from the target populations
  For example, wearing an eye mask is not a good surrogate for understanding the needs of the no-vision/low-vision populations
Consistent with good design process, accessible design begins at the requirements phase
Pursue an "accessible" solution that is consistent with a mainstream solution – accessible design adds value for all users
Slide 29

## Slide 30: Best Practices Status
First iteration focused primarily on packaging and instructions
  This document is now available on the U.S. Access Board website
  Approximately 1200 website visits in last 60 days
Comprehensive version is scheduled for publication in May 2023
Documents available both accessible online HTML and PDF
Source: https://www.nibib.nih.gov/covid-19/radx-tech-program/listening-session/agenda
Slide 30

## Slide 31: Thank You
Slide 31

## Slide 32: References
ADA Standards for Accessible Design. (2010). US Department of Justice Civil Rights Division.
ANSI/AAMI HE75:2009(R)2018 Human Factors Engineering - Design of Medical Devices. (2018).
Applying Human Factors and Usability Engineering to Medical Devices. (2016). U.S. Department of Health and Human Services, Food and Drug Administration, Center for Devices and Radiological Health, Office of Device Evaluation
Clinical Laboratory Improvement Amendments of 1988 (CLIA) Waiver Applications for Manufacturers of In Vitro Diagnostic Devices. (2020). US Food and Drug Administration.
Design Considerations for Devices Intended for Home Use. (2014). US Food and Drug Administration.
Do It By Design - An Introduction to Human Factors in Medical Devices. (1996). US Food and Drug Administration.
Federal Plain Language Guidelines. (2011). In PlainLanguage.gov.
Human Factors Implications of the New GMP Rule Overall Requirements of the New Quality System Regulation. (1997). US Food and Drug Administration.
Web Content Accessibility Guidelines (WCAG) 2.1 W3C Recommendation. (2018).
Slide 32